## Slide 1
MS Thesis Defense,
CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Presenter:
Chok Meng Yip
Presentation Location: Jabara Hall, ROOM: 260
Presentation Date: 07/17/2014

## Slide 2: About Me
I am Chok Meng Yip, majoring in Computer Networking with thesis under Dr. Abu Asaduzzaman
Lab Assistant at CAPPLab
  Embedded Systems
  Parallel Programming
Co-author of publications:
  “An effective CUDA based simulation for lightning strike protection on nanocomposite materials” in Southeastcon 2013
  “Fast Effective Deterministic Primality Test Using CUDA/GPGPU”, in International Journal of Computers & Technology (IJCT), Vol. 12, No. 3, pp. 3738-3746, Jan. 2014.
  “CUDA/C Based ‘Green’ Technology for Very Fast Analysis of Nanocomposite Properties,” in SAMPE Tech 2013 Conference, Wichita, Kansas, Oct. 21-24, 2013.
  “Fast, Effective, and Adaptable Computer Modeling and Simulation of Lightning Strike Protection on Composite Materials,” in IEEE SoutheastCon Conference 2013, Jacksonville, Florida, April 4-7, 2013.
  “A Promising CUDA-Accelerated Vehicular Area Network Simulator Using NS-3,” under review, in 33rd IEEE International Performance Computing and Communications Conference (IPCCC), Austin, TX, Dec. 5-7, 2014.

## Slide 3: Improved VANET Simulator
Outline ►
  Introduction
  Motivation
  Proposal
  Evaluation
  Results
  Conclusions
Q U E S T I O N S ?
Any time, please.

## Slide 4: Introduction
Vehicular Area Networking (VANET)
Wireless Networking Technologies
  Physical Layer
  Medium Access Control
  802.11p
Mobility Modelling
  Vehicular Area Networks Types
  Driving Behavior
Applications
  Accident prevention

## Slide 5: Wireless Networking
Physical Layer
Modulation
  Encode
Demodulation
  Decode
Digital <-> Analog
Signal Modulation[1]

## Slide 6: Wireless Networking (+)
Physical Layer (+)
Signal-Noise Ratio
SNR <-> Bit Rate
Distance
  Fixed Frequency
Signal Modulation[1]

## Slide 7: Wireless Networking (+)
Medium Access Control
Coordinates nodes
Medium Sharing
High usage
Distributed Coordinated Function[2]

## Slide 8: Wireless Networking (+)
IEEE 802.11p
Intelligent Transportation System
802.11p
5.8Ghz Allocated 75Mhz
Service Channels
Control Channels
Frequency (Ghz) | 5.850 | 5.860 | 5.870 | 5.880 | 5.890 | 5.900 | 5.910 | 5.920
Channel Number |  | 172 | 174 | 176 | 178 | 180 | 182 | 184
Usage | Spacing | Critical Safety | Service Channels |  | Control Channel | Service Channels |  | Public Safety

## Slide 9: Introduction
Mobility Modelling
Driving Behavior
Acceleration
Lane Change
Merits
Politeness
Treiber Intelligent Driving Model
V current velocity
V0 intended velocity

## Slide 10: Introduction
Applications
Influence Driving Behavior
  Beyond visible range
  Line of sight
Communication Types
V2V
V2I
V2x

## Slide 11: Wireless Networking
Applications-An Example
Vehicle Breakdown
Driver Alerted
Driver Informs to Change Lane

## Slide 12: CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Outline ►
  Introduction
  Motivation
  Proposal
  Evaluation
  Experimental Results
  Conclusion
Q U E S T I O N S ?
Any time, please.

## Slide 13: Motivation
Optimize Network Performance
Simulation
MAC
Signal Strength
Placement of Nodes
Data dissemination

## Slide 14: Problem Statement
Simulators
Current Available Technology
MoVes
  Distributed Systems
  Many Computers
  Expensive
Moritz
  Mathematical Optimization
  15% Less accurate
Traditional Simulator
  Slow

## Slide 15: Problem Statement
NS-3 Simulator
Open Source
Accurate Models
Weingartner et.al [3] -Fastest Simulator
 | OMNet++ | NCTuns | NS-3
Implementation | GUI | GUI + Backend | Backend Only
Simulation Speed [3] | Baseline | Fast | Fastest
Source Model | Open | Closed | Closed

## Slide 16: Problem Statement
NS-3 VANET Simulator
Event based simulator
Hadi Arbabi & Michelle Wiegle
Models
  Treiber IDM
  NS-3 Wireless Stack
NS-3 Modules

## Slide 17: CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Outline ►
  Introduction
  Motivation
  Proposal
  Evaluation
  Experimental Results
  Conclusion
Q U E S T I O N S ?
Any time, please.

## Slide 18: Traditional Simulator
Vehicular Modelling
Stores data in Linked List
No easy parallelization method
Computationally Expensive

## Slide 19: Proposed Simulator
Proposed NS-3 Simulator
Initialization
Position Matrix
Velocity Matrix
Iteration
Acceleration
Apply Matrix
Copy Distance

## Slide 20: Proposed Simulator (+)
CUDA NS-3 VANET Simulator
Change Data structure to Matrix
Collect all data before computing
GPU to speed up
  Many Cores
Same Equation

## Slide 21: CUDA
CUDA GPGPU
Compute Unified Device Architecture
SIMD
Device memory
Divide Data into
  Grid
  Block
  Threads
Shared Memory for each block
Programmers (Logical) perspective

## Slide 22: CUDA(+)
CUDA GPGPU
GPU Core
Many Cores
Hardware (Physical) perspective

## Slide 23: Proposed Simulator (+)
Position Matrix
Easy to Compute for GPU
Easy to retrieve from CPU
Pt[0] – Position of node 0

## Slide 24: Proposed Simulator (+)
Distance Matrix
Computes distance between all nodes
Performed in GPU
__global__ void computeDistanceMatrix(Vector3D *a, Vector3D *b, double *c, int numberOfNodes){ .. if ( (i<numberOfNodes) && (j < numberOfNodes)){ c[i*numberOfNodes + j] = sqrt(dx*dx + dy*dy + dz*dz); } }

## Slide 25: Proposed Simulator (+)
Proposed NS-3 Simulator
Uses same input
Generates same output
Wireless: Only need Distance between nodes

## Slide 26: CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Outline ►
  Introduction
  Motivation
  Proposal
  Evaluation
  Experimental Results
  Conclusion
Q U E S T I O N S ?
Any time, please.

## Slide 27: Evaluation
Correctness
    P0 initial position
    M0 initial movement
    P1 after first iteration
    D1 distance after 5 iterations
    P5 after 5 iteration

## Slide 28: Evaluation
Compare to CPU
Same result as CPU
Node Number | X position |  | Y position | 
 | Before | After | Before | After
Node 1 | 1 | 16 | 1 | 1
Node 2 | 3 | 21 | 1 | 1
Node 3 | 5 | 23 | 1 | 1
Node4 | 7 | 25 | 1 | 1
Node 5 | 9 | 27 | 1 | 1

## Slide 29: CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Outline ►
  Introduction
  Motivation
  Proposal
  Evaluation
  Experimental Results
  Conclusion
Q U E S T I O N S ?
Any time, please.

## Slide 30: Experimental Results
Platforms
 | Supercomputer | Workstation
CPU | AMD Opteron 6134 | Intel Xeon E5506
CPU Cache Size | 512KB | 4096KB
Cores | 32 | 8
Clock Speed | 2.3 Ghz | 2.13 Ghz
RAM Size | 64GB | 12GB
GPU | NVidia Tesla K20m | NVidia Tesla C2075
GPU Architecture | Keper | Fermi
GPU Core Clock | 0.71GHz | 1.15GHz
GPU Memory Size | 5GB | 6144MB
GPU Cores | 2496 | 448

## Slide 31: Experimental Results
Isolated Workload

## Slide 32: Experimental Results
Isolated Workload
Traditional Simulator
  Time increase Exponentially
Proposed Simulator
  Minimal Time Increase
75x Speed up

## Slide 33: Experimental Results
Isolated Workload

## Slide 34: Experimental Results
Isolated Workload
Traditional Simulator
  Time increases linearly
Proposed Simulator
  Time increases by factor

## Slide 35: Experimental Results(+)
Full Workload

## Slide 36: Experimental Results(+)
Full Workload
Traditional
  Time increases linearly
Proposed
  Converges to CPU Time

## Slide 37: Experimental Results(+)
Energy Consumption- Isolated Workload
Traditional
  Exponential increase
Proposed
  Small Factor increase
Chart: Isolated Workload- Energy vs Number of Nodes
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
Traditional | 1.7777 | 4.0105 | 7.1565 | 11.2515 | 16.1135 | 21.8822 | 28.6878 | 36.4682 | 44.6615 | 54.171
Proposed | 0.16587 | 0.311 | 0.41985 | 0.50278 | 0.62718 | 0.67383 | 0.8397 | 0.91227 | 1.047 | 1.1507

## Slide 38: Experimental Results(+)
Energy Consumption- Isolated Workload
Traditional
  Linear increase
Proposed
  Exponential Increase

## Slide 39: CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Outline ►
  Introduction
  Motivation
  Proposal
  Evaluation
  Experimental Results
  Conclusion
Q U E S T I O N S ?
Any time, please.

## Slide 40: Conclusion
VANET is a complex system
Simulation assists network designers to design VANET network
VANET is computationally expensive due to complexity

## Slide 41: Conclusion (+)
By modifying the NS-3 data-structure, we can parallelize the process
Using NVIDIA CUDA, we achieve up 75x speed up
Data-Dependency on CPU
Enhance more modules to reduce dependence on CPU

## Slide 42: Future Extensions
Enhance NS-3 Modules:
  Further improve VANET simulator throughput by using CUDA in more modules
Self Optimizing Simulator:
  Simulator optimize input parameters by using output as feedback.
Data Regrouping:
Improve CUDA effectiveness by using data regrouping based on locality principle.

## Slide 43: Questions?

## Slide 44: CUDA ACCELERATED LARGE SCALE VEHICULAR AREA NETWORK SIMULATOR
Thank you.
Chok Meng Yip
cxyip1@wichita.edu

## Slide 45: References
Gronemeyer, Steven A., and Alan L. McBride. "MSK and offset QPSK modulation." Communications, IEEE Transactions on 24, no. 8 (1976): 809-820.
Bianchi, Giuseppe. "Performance analysis of the IEEE 802.11 distributed coordination function." Selected Areas in Communications, IEEE Journal on 18, no. 3 (2000): 535-547.