## Slide 1: A Fast Flexible Simulation Platform for Multi-Core Systems
Committee Members:
Dr. Abu Asaduzzaman
Dr. Ravi Pendse
Dr. Mehmet Bayram Yildirim - Phanendra S. N. Gavara

## Slide 2
Outline
Problem description
Thesis contributions
Why simulation technique?
Brief introduction to multicore processors
Proposed simulation tool
Evaluation
Conclusions
Future work

## Slide 3
Problem Description
Multicore systems are now a days mainly method against the power consumption and high-performance
Design and research on such physical systems are confined to research industries:
    Intel Polaris- 80 Core Terascale Chip, 80 cores[1]
    IBM BladeCenter System-QS22/LS21 has 122,400 cores[2]
There is no suitable software/firmware that meets our research needs in multicore systems
[1] http://software.intel.com/en-us/articles/developing-for-terascale-on-a-chip-first-article-in-the-series/?wapkw=Teraflop%20Research%20Chip
[2] http://www-05.ibm.com/fr/events/campus_paris/Francois_Thomas.pdf

## Slide 4
Problem Description Cont…
Any few traces found are specific to their own design and imposes copy right issues
Hence there is a need for flexible simulation platform which is:
    Suitable to model any multicore system
    Flexible to perform the top level pre-design analysis
    Can be used for the future complex architectures

## Slide 5
Thesis Contributions
Develop a fast flexible simulation platform for multicore systems
Using the platform, implement a serial/parallel processing system for the top level analysis of performance and power
Analyze the sequential and parallel executions of the target workloads

## Slide 6
Evaluation Techniques
Performance evaluation methodologies in proceedings of the international symposium on computer architecture
J.J. Yi, L. Eeckhout, D.J. Lilja, B. Calder, L.K. John, and J.E. Smith. The Future of Simulation: A Field of Dreams? The IEEE Computer Society, pages 22-29,2006.

## Slide 7: Why Simulation Technique?
Measurement | Analytical | Simulation
Physical system Cost involved Not Flexible Not Scalable | Not required Less cost Not Flexible Scalable | Not required Less cost Flexible Scalable
  Direct measurement is a post-design step and not useful for systems under design.
  Analytical method is good for preliminary design but not suitable for assessing detailed design trade-offs and complex systems.

## Slide 8
Current Research & Tools
        MIT Hornet - Targeted for cycle accurate simulation for up to 1000 Cores
        Graphite Multicore Simulator - Deep level analysis
        FastMP - Aimed at speeding up multi-core simulation runtimes
        VirtualSim
        SimuLink
        MicroSaint etc.

## Slide 9: MULTI-CORE ARCHITECTURE

## Slide 10
A Multicore Processor
In which, cores are integrated onto a single circuit known as a Chip Multicore processor.
Composed of two or more independent cores (or CPUs) typically up to 32 [1].
A Manycore Processor
Cores are large in number, likely requires a Network-on-Chip architecture.
Threshold is up to hundreds and several thousands of cores
[1] Many-core processor, 2008. http://software.intel.com/en-us/articles/many-core-processor/

## Slide 11
Current & Future Market
Current publicly available multicore processors have 2 to 4 cores [i.e. Amd x2 and x4 series, Intel i7 (8 threads)]
Future we will see up to hundreds and several thousands of cores for the commercial purpose like Could Services , Heavy Virtualization, Super Computers etc.
http://ark.intel.com/products/63698/Intel-Core-i7-3820-Processor-%2810M-Cache-3_60-GHz%29

## Slide 12: Dual Core Chip
The two cores are two separate processors plugged into the same socket
Theoretically twice as powerful as a single core processor.
Performance gains are said to be about fifty percent: Therefore one-and-a-half times as powerful as a single core processor.
http://www.xda-developers.com/android/first-htc-sensation-rom-with-enabled-full-dual-core-support/

## Slide 13: Multicore Chip
Core 1
Core 2
Core 3
Core 4
http://www.teknocrat.com/core-vs-cpu-socket-chip-processor-difference-comparison.html

## Slide 14
Core 1
Core 2
Core 3
Threads
Threads
Threads
[1] http://groups.csail.mit.edu/carbon/?page_id=111
[1]
Threads Running Concurrently (in Parallel)

## Slide 15
Threads Assignment
http://home.dei.polimi.it/gpalermo/doc/PIN.pdf

## Slide 16: PROPOSED SIMULATION TOOL

## Slide 17: Design Goals
Preprocessing Tools
Multi-Core Simulation Platform
Synthetic Workloads
Results/
Analysis
Add additional Functionality (Optional)
Applications

## Slide 18
Serial/Parallel Processing
N Cores
I1, D1 Cache
L2 Cache
Interval
Input
    Independent/Parallel workloads
    Dependent/Serial workloads
Output
    Total Processing Time
    Total Power
FCFS (First Come, First Serve) System
Provision for Arrival time and Priority

## Slide 19
Workloads
In computer industry, a workload is the real task done by the CPU
Synthetic workloads are the abstraction of real workload
In multicore, workloads are characterized into:
  Serial/Dependent
  Parallel/Independent

## Slide 20: Serial Workload
Job_Num | Num_of_Threads | Thread_Duration (Units) | Arrival_Time (Units) | Priority
0001 | 002 | 003 | 0.00 | 1
0001 | 003 | 004 | 0.00 | 1
Same job could have different thread types
Each job could be real-time application
Each applications is divided into multiple threads

## Slide 21
Parallel Workload
Each job could be real-time application
Each applications is divided into multiple threads
Job_Num | Num_of_Threads | Thread_Duration (Units) | Arrival_Time (Units) | Priority
0001 | 002 | 002 | 0.00 | 1
0002 | 008 | 001 | 0.00 | 1
0003 | 002 | 002 | 0.00 | 1
0004 | 004 | 001 | 0.00 | 1
0005 | 001 | 007 | 0.00 | 1

## Slide 22
Raw Workload
Each job could be real-time application
Duplicate jobs are interdependent
Job_Num | Num_of_Threads | Thread_Duration (Units) | Arrival_Time (Units) | Priority
0001 | 002 | 002 | 0.00 | 1
0002 | 008 | 001 | 0.00 | 1
0003 | 003 | 003 | 0.00 | 1
0003 | 004 | 001 | 0.00 | 1
0004 | 009 | 001 | 0.00 | 1
0005 | 006 | 003 | 0.00 | 1
0006 | 002 | 003 | 0.00 | 1
0006 | 004 | 006 | 0.00 | 1

## Slide 23
Flowchart of Executions
User Inputs: Number of Cores, Interval, Mode, Input and Output File Name
Start
Initialization: Processor, Cores & other Parameters like Job, Queue etc.
Mode P/S?
B
A
Process the Input file into Sequential & Parallel workload files
Serial
Parallel
CP-1

## Slide 24
Serial Execution
A
Compute the total number of threads and delays associated with each job and write the new jobs to a Serial_to_Prallel workload file.
Append the jobs of Serial_to_Prallel file to the Parallel _Input file for the analysis of total processing time and power in a multi-core environment.
C
CP-2

## Slide 25
P
A
R
A
L
L
E
L
E
X
E
C
U
T
I
O
N
C
Based on the Multicore System, jobs are loaded from the Parallel _Input file to the Input_Queue
Threads are distributed among the available free cores, Interval timer is set and the Avl_Free_Cores are updated
Allocate/Busy
Core N-1
Allocate/Busy
Core 2
Allocate/Busy
Core 1
Allocate/Busy
Core N
Thread_Durations are updated with the Interval duration and Cores are set free accordingly
Core N
Core N-1
Core 2
Core 1
De-allocate/Free
De-allocate/Free
De-allocate/Free
De-allocate/Free
Parameters like Upd_Free_Cores, Processing_Time, Power_Cnsmptn are updated and logged to a file called Results
Load Jobs?
B
No
Yes
Total Processing_Time & Power_Cnsmptn are computed and written to an output file
Stop
B
CP-4
CP-3

## Slide 26
Code
Struct processor{
unsigned int num_of_cores;
typeCore processor_core[];
unsigned int cl2_size;
};
typedef struct processor typeProcessor;
Struct Core{
unsigned int i1_size;
unsigned int d1_size;
unsigned int flag;//0 for free, 1 for empty
};
typedef struct Core typeCore;

## Slide 27
Job_Num | Num_of_Threads | Thread_Duration (Units) | Arrival_Time (Units) | Priority
0001 | 002 | 002 | 0.00 | 1
0002 | 008 | 001 | 0.00 | 1
0003 | 003 | 003 | 0.00 | 1
0004 | 004 | 001 | 0.00 | 1
0005 | 002 | 008 | 0.00 | 1
0006 | 009 | 001 | 0.00 | 1
0007 | 006 | 003 | 0.00 | 1
0008 | 002 | 003 | 0.00 | 1
0009 | 004 | 006 | 0.00 | 1
0010 | 005 | 005 | 0.00 | 1
Parallel workload on a 16 Core System

## Slide 28
Job_Num | Num_of_Threads | Thread_Duration (Units) | Arrival_Time (Units) | Priority
0001 | 002 | 002 | 0.00 | 1
0002 | 008 | 001 | 0.00 | 1
0003 | 003 | 003 | 0.00 | 1
0004 | 004 | 001 | 0.00 | 1
0005 | 002 | 008 | 0.00 | 1
0006 | 009 | 001 | 0.00 | 1
0007 | 006 | 003 | 0.00 | 1
0008 | 002 | 003 | 0.00 | 1
0009 | 004 | 006 | 0.00 | 1
0010 | 005 | 005 | 0.00 | 1
Parallel workload on a 32 Core System

## Slide 29: EVALUATION

## Slide 30: Checkpoint Evaluation
 | Raw Input | Serial Workload | Parallel Workload | Total Processing Time | Total Power
Checkpoint-1 | I | O1 | O2 | - | -
Check Point-2 | - | I | O3 | - | -
Check Point-3 | - | - | O3+O2 | - | -
Check Point-4 | - | - | I |  | 

## Slide 31
Checkpoint-1:
  Raw workloads  Serial/Dependent (O1) & Parallel/Independent (O2) workload files
Checkpoint-2:
  Output of Checkpoint-1 (O1) Parallel/Independent (O3)
Checkpoint-3:
  Output of checkpoint-2 (O3)  Parallel/Independent (O2+O3)
Checkpoint-4:
  Output of checkpoint-3 (O2+O3)  Evaluate total processing time and power

## Slide 32
Sequential Workload Analysis

## Slide 33
Logic Based Distributed Routing Architecture
Core 1(0,0) wants to communicate with Core 15(1,6)
Path taken: (0,0), (0,0). (1,0). (1,4), (1,6)
Job_Num | Num_of_Threads | Thread_Duration
0001 | 002 | 002
0001 | 003 | 001
Abstraction of actual work to Synthetic Workload
Rodrigo, S.; Medardoni, S.; Flich, J.; Bertozzi, D.; Duato, J.; “Efficient implementation of distributed routing algorithms for NoCs Computers & Digital Techniques, IET Volume: 3, Issue: 5, DOI: 10.1049/iet-cdt.2008.0092, page(s): 460-475.2009.

## Slide 34
[Chaturvedula, 2011] Proposed Architecture
Chaturvedula, R.;” Designing Multi-Core Architecture Using Folded Torus Concept to Minimize the Number of Switches”, Thesis in Masters of Science, Florida Atlantic Wichita State University, Dec, 2011.
Solid nodes Switching Nodes
Empty nodes Computing Nodes
Striped node Switching & Computing Node

## Slide 35: Communication paths for LBDR and [Chaturvedula, 2011] Proposed Architectures in the case of 16 Core
Chaturvedula, R.;” Designing Multi-Core Architecture Using Folded Torus Concept to Minimize the Number of Switches”, Thesis in Masters of Science, Florida Atlantic Wichita State University, Dec, 2011.
 | Source-Destination | LBDR | [Chaturvedula,2011] Model
Case 1 | Node 2 – Node 15 | 2, 1(Sw), 6(Sw), 11(Sw), 15 | 2, 1(Sw), 13(Sw) , 15
Case 2 | Node 3- Node 14 | 3, 1(Sw), 6(Sw), 11(Sw), 14 | 3, 1(Sw), 13(Sw), 14
Case 3 | Node 7 – Node 15 | 7, 6(Sw), 11(Sw), 15 | 7, 11(Sw), 15
Case 4 | Node 2 – Node 10 | 2, 1(Sw), 6(Sw), 10(Sw) | 2, 6(Sw), 10

## Slide 36
Job_Num | Num_of_Threads | Thread_Duration (Sec) | Arrival_Time | Priority
0001 | 002 | 002 | 0.00 | 1
0001 | 003 | 001 | 0.00 | 1
0002 | 002 | 002 | 0.00 | 1
0002 | 003 | 001 | 0.00 | 1
0003 | 002 | 002 | 0.00 | 1
0003 | 002 | 001 | 0.00 | 1
0004 | 002 | 002 | 0.00 | 1
0004 | 002 | 001 | 0.00 | 1
Derived workloads for LBDR Model
Job_Num | Num_of_Threads | Thread_Duration (Sec) | Arrival_Time | Priority
0001 | 002 | 002 | 0.00 | 1
0001 | 002 | 001 | 0.00 | 1
0002 | 002 | 002 | 0.00 | 1
0002 | 002 | 001 | 0.00 | 1
0003 | 002 | 002 | 0.00 | 1
0003 | 001 | 001 | 0.00 | 1
0004 | 002 | 002 | 0.00 | 1
0004 | 002 | 001 | 0.00 | 1
Derived workloads for [Chaturvedula, 2011] Model

## Slide 37
Chart: Delay analysis for 16 nodes
| Case 1 | Case 2 | Case 3 | Case 4
LBDR | 7 | 7 | 6 | 6
Simulation | 7 | 7 | 6 | 6
Column1
LBDR and Simulation results are very similar

## Slide 38
Chart: Delay analysis for 16 nodes
| Case 1 | Case 2 | Case 3 | Case 4
[Chaturvedula, 2011] Model | 6 | 6 | 5 | 6
Simulation | 6 | 6 | 5 | 6
Column1
[Chaturvedula, 2011] and Simulation results are very similar

## Slide 39
Parallel Workload Analysis

## Slide 40
Job_Num | Num_of_Threads | Thread_Duration | Arrival_Time | Priority
0001 | 002 | 020 | 0.00 | 1
0002 | 008 | 006 | 0.00 | 1
0003 | 007 | 018 | 0.00 | 1
0004 | 004 | 010 | 0.00 | 1
0005 | 004 | 028 | 0.00 | 1
0006 | 007 | 009 | 0.00 | 1
0007 | 003 | 001 | 0.00 | 1
0008 | 015 | 025 | 0.00 | 1
0009 | 004 | 005 | 0.00 | 1
0010 | 005 | 005 | 0.00 | 1
0011 | 010 | 007 | 0.00 | 1
0012 | 001 | 060 | 0.00 | 1
0013 | 007 | 028 | 0.00 | 1
0014 | 002 | 041 | 0.00 | 1
0015 | 015 | 001 | 0.00 | 1
Parallel Workload

## Slide 41: Total Processing Time Analysis
Chart: Total processing time for various core systems
| 16 Core | 32 Core | 64 Core | 128 Core | 160 Core | 192 Core
Duration | 134 | 83 | 65 | 60 | 60 | 60
Load Interval = 1 Unit
High performance results in128 core system

## Slide 42: Total Power Analysis
ASSUMPTIONS:
Core Busy = 0.1 Unit
Core Idle = 0.05 Unit
Core Off = 0 Unit
Chart: Total Power Analysis
| Core 16 | Core 32 | Core 64 | Core 128 | Core 160 | Core 192
On/Off | 127.5 | 127.5 | 127.5 | 127.5 | 127.5 | 127.5
On/Idle/Off | 176.35 | 187 | 271.75 | 399.46 | 543.75 | 685.72
Series 3
On/Off condition results in constant power utilization
On/Idle/Off condition results in increased power utilization with the increase in number of cores

## Slide 43: Overall Observations
128 core system results in high performance, but with high power utilization
64 core system provides an equivalent performance and with less power utilization
For the target workloads, any system greater than 128 is considered to have high availability and poor power utilization

## Slide 44
A fast flexible Multi-Core Simulation Platform has been introduced
Using the platform, implemented a Serial/Parallel processing system
Analyzed the sequential and parallel executions of the target workloads
Conclusions

## Slide 45
Efficient algorithms can be developed for the cache analysis purpose
Efficient algorithms can be developed for various core allocation strategies
Efficient multi-core route algorithms can be developed
Web interface and cloud services can be provided for the future researchers
Future work

## Slide 46
Thank you
Phanendra Sandeep Naidu Gavara
myWSU ID: J667T676
Phone: (316) 841 3767